## Slide 1: BAYESIAN TREATY MONITORING: PRELIMINARY REPORT
The method of Double-differencing (Waldhauser & Ellsworth, 2000) relocates events using precise arrival-time difference information obtained through waveform matching, while considering correlated travel-time residuals.
We formulate a Bayesian model with similar properties: our model integrates information from picked arrival times as well as arrival-time differences, and explicitly models correlated residuals as a function of variation in the underlying slowness field (Rodi and Meyers, 2007):
The slowness field is modeled as a Gaussian process, which induces an equivalent Gaussian process on the travel-time residuals. This connection allows inference to recover a posterior distribution over event locations as well as the slowness field:
Inference is through Markov Chain Monte Carlo (Metropolis-Hastings w/ Gaussian proposals).
Introduction
Stuart J. Russell,1 Stephen C. Myers,2 Nimar S. Arora,1 David A. Moore,1 and Erik Sudderth3
University of California, Berkeley,1 Lawrence Livermore National Laboratory,2 and Brown University3
Background: Detection-based Bayesian monitoring
Global seismic monitoring for the Comprehensive Nuclear-Test-Ban Treaty (CTBT) aims to recover the time, location, depth, and magnitude for all seismic events in the magnitude range of interest.
Data from the International Monitoring System (IMS) are processed in real time at the International Data Centre (IDC) in Vienna. Our goal is to improve the sensitivity and accuracy of automated processing at IDC.
Signal-Based vs. Detection-Based Monitoring
Signal-based Bayesian monitoring
CONCLUSIONS
Prior results suggest that Bayesian monitoring is a promising technique for analyzing streams of parametric detections from multiple stations to form a global event bulletin and may be preferable to existing deployed methods for global association.
Our current work, in its very early stages, is aimed at extending Bayesian monitoring with generative models of waveform envelopes to improve detection and association and performing joint inference of event locations and slowness fields to improve localization accuracy.
REFERENCES
Arora, Nimar S., Stuart J. Russell, Paul Kidwell, and Erik Sudderth, “Global seismic monitoring as probabilistic inference.”, In Advances in Neural Information Processing Systems 23, MIT Press, 2011.
Milch, B., Marthi, M., Sontag, D. Russell, S., Ong, D. L., and Kolobov., A. (2005). BLOG: Probabilistic Models with Unknown Objects. In Proc. IJCAI-05, Edinburgh, Scotland.
Myers, S.C., G. Johannesson, and W. Hanley (2007). A Bayesian hierarchical method for multiple-event seismic location. Geophys. J. Int., 171, 1049-1063.
Oh, S., Russell, S., and Sastry, S. S. (2009). Markov Chain Monte Carlo Data Association for Multi-Target Tracking. IEEE Transactions on Automatic Control, 54(3), 481-497.
Rodi, W. L., and S. C. Myers (2007), Modeling travel-time correlations based on seismicity kernels and correlated velocity anomalies, Paper presented at 29th Monitoring Research Review: Ground-Based Nuclear Explosion Monitoring Technologies, Denver, Colorado.
Schaff, D. P., Bokelmann, G. H. R., Ellsworth, W. L., Zanzerkia, E., Waldhauser, F., & Beroza, G. C. (2004). Optimizing Correlation Techniques for Improved Earthquake Location. Bull. Seism. Soc. Amer, 94(2), 705-721.
Schultz , C.A., S.C. Myers, J. Hipp, and C. Young (1998). Nonstationary Bayesian kriging: a predictive technique to generate corrections for detection, location, and discrimination, Bull. Seismol. Soc. Am., 88, 1275-1288.
Waldhauser, F. and Ellsworth, W. L. (2000). A Double-Difference Earthquake Location Algorithm: Method and Application to the Northern Hayward Fault, California. Bull. Seism. Soc. Amer., 90(6), 1353-1368.
Zhang, H., & Thurber, C. H. (2003). Double-difference tomography: The method and its application to the Hayward fault, California. Bulletin of the Seismological Society of America, 93(5), 1875.
ACKNOWLEDGEMENTS
We gratefully acknowledge the support of DTRA for this work; also the support of CTBTO for the work on NET-VISA and the technical cooperation of CTBTO personnel including Ronan Le Bras and Jeff Given. We thank Sheila Vaidya of LLNL and Ola Dahlman, former Chair of CTBTO Working Group B, for their moral support and encouragement in this project.
NET-VISA is a probabilistic generative model of seismic events, their propagation and detection. Also, a model of noise detections.
Bayesian Double-Differencing
Results on one week of data (trained on 2.5 months)
NET-VISA is a detection-based Bayesian monitoring system whose performance is limited by the classical, bottom-up, threshold-based detections algorithms used in station processing.
SIG-VISA, a signal-based system, will use generative models that span the range from events to waveform traces. It will have several qualitative advantages over NET-VISA, potentially yielding a significant improvement in detection performance
Blue dots and triangles are primary seismic stations.
events
detections
waveform signals
SEL3
station
processing
NET-VISA
SIG-VISA
model
inference
model
inference
Bayesian monitoring with a generative approach
P(world) describes prior probability for what is (events)
P(signal | world) describes forward model
(propagation, measurement, etc.)
Detection-based Bayesian monitoring:
P(world | f (signal)) ~ P(f (signal) | world) P(world)
where f (signal) = set of all detections
Signal-based Bayesian monitoring:
P(world | signal) ~ P(signal | world) P(world)
Travel times
Travel times
Seismic Event
Seismic Event
Station 1
detections
Station 1
noise
Station 2
detections
Station 2
noise
Detected at
Station 1?
Detected at
Station 2?
mb range | Number of Events | SEL3 |  | NET-VISA | 
 |  | Recall (%) | Error (km) | Recall (%) | Error (km)
0-2 | 74 | 64.9 | 101 | 86.5 | 101
2-3 | 36 | 50.0 | 186 | 77.8 | 159
3-4 | 558 | 66.5 | 104 | 86.4 | 115
>4 | 164 | 86.6 | 70 | 93.3 | 78
The model consists of various probability distributions, which include:
A distribution for seismic event locations, which includes natural seismicity and manmade seismicity (assumed uniform).
The detection probability of an event depends only on event magnitude, depth, and distance to station.
The residual distribution for the travel time, azimuth, and slowness are mostly modeled as Laplacian distributions.
Arrival-Time Picks
Arrival-time Differences
(waveform matching)
Event Locations
Slowness Field Tomography
Bayesian Inference (MCMC)
True event locations and slowness field
(simulated data)
Expected event locations and
slowness field , recovered from arrival time picks observed at stations in the four corners.
Variance/uncertainty in slowness field posterior (darker is higher)
Bayesian/probabilistic formulation makes it easy to include additional inputs, such as arrival-time differences from waveform matching / cross-correlation techniques.
Results on simulated data show decreased error in both absolute and relative event locations, as compared to double-differencing and to a baseline inversion which assumes independent residuals.
Image from Schaff et. al. (2004)
A signal-based model encodes the joint distribution of the waveform traces at each station given the event parameters for all hypothesized events.
We overlay background noise models, independent for each station, with event-generated waveforms of the contributions of each phase type.
A simple approach involves a low-dimensional parametric envelope descriptor (e.g., triangular or paired-exponential, cf. Huseby et al., 1998) whose arrival time, amplitude, and spread depend on event distance & magnitude:
Actual envelopes are not well-modeled by template + iid noise. We model large-scale variation in envelope shape as the product of a mean envelope (magnitude and distance dependent), and a stochastic modulation signal:
A simple modulation model, which we will ultimately learn from historical data, is based on a random linear combination of Fourier basis functions:
A basic model of envelope variation would assign each event an independent sampled log-modulation signal, using a Gaussian prior on the basis coefficients
Envelope (or waveform) shape is highly repeatable across events with the same location and type. A nonparametric extension, based on Gaussian processes, captures correlations among event envelopes that decay with distance (analogous to correlation matching).
observedEventEnvelope = meanEnvelope x exp(eventSpecificModulation)
Sampled Log Envelope Modulation Signal
Mean Envelope and Observed Envelope
Historical Envelope and Sample at Larger Distance
Historical Envelope and Sample at Close Distance
The rates at which correlations decay with distance will also be calibrated from historical training data.