## Slide 1: A model of seismic coda arrivals to suppress spurious events.
Nimar Arora
Stuart Russell
UC, Berkeley
EGU – 2012-6763
SM3.1-AS4.20
April 24, 2011
Acknowledgements: Heidi Anderson Kuzma, Tony Dear

## Slide 2: NET-VISA
NETwork Processing – Vertically Integrated Seismic Analysis
  NET-VISA automatically analyzes arrivals from the International Monitoring System (IMS) of the Comprehensive Test Ban Treaty Organization (CTBTO)
  It is designed to identify and locate seismic events using the time, magnitude, azimuth and slowness of pre-computed arrivals
  NET-VISA operates by probabilistic inference, applied to a decomposable physics-based model in which empirical uncertainty is made explicit
  P(Events | Arrivals) α P(Arrivals | Events) *P(Events)
Prior
Bulletin
Model
Notes: Model = propagation + detection

## Slide 3: Outline
Background: NET-VISA baseline
Coda arrivals
  Problem
  Refined model
  Results

## Slide 4: NET-VISA model components
Events
Seismic Wave Propagation
Waveforms at seismometers
NET-VISA
Inference
Arrivals
Station Processing
Station Noise
Detected?
Physics
Inference

## Slide 5: Generative Model – Event Location
Notes: Learned with historical data and mixed with a uniform distribution to allow for explosions.

## Slide 6: Generative Model – Detection Probability
P phase, station 6
S phase, station 6
P(Detected) = Logistic(f(distance,magnitude,depth))
Notes: The detection probability depends on the distance and magnitude (also depth, not shown for simpicity).
In contrast, seismologists build a detection model based on histograms of detections at every point on the earth – clear tendency to overfit where there is no prior history!

## Slide 7: Generative Model – Arrival Time
Arrival time = Event time + IASPEI + corrections + Laplacian residual
Notes: This is a for-example.

## Slide 8: Inference Overview
Max a-posteriori (MAP) seismic event bulletin
Probability-driven search over association/phase-label/location/depth/time/magnitude
Easily parallelizable – runs in real time on Tohoku and Sumatra
Notes: We are trying to find the MAP bulletin, because this is what seismologists expect to see.
The basic approach is a heuristic search which moves forward in time.

## Slide 9: Outline
Background: NET-VISA baseline
Coda arrivals
  Problem
  Refined model
  Results

## Slide 10: Coda arrivals
Direct Arrivals
Coda Arrivals
Notes: But the picture is not very rosy!

## Slide 11: NET-VISA finds shadow events from the coda arrivals.
1 real event,
4 shadow events
Notes: Windows: python debug.py 490 visa 1997
5297214

## Slide 12: A coda model was introduced to NET-VISA
Events
Seismic Wave Propagation
Waveforms at seismometers
Arrivals
Station Noise
Detected?
Coda Model

## Slide 13: Coda Model I: Probability of coda arrivals depends on prior arrival’s amplitude
Coda occurs after direct arrival
Log(amp)
After coda arrival
Probability
Log(amp)
Detector finds arrivals based on ratio of Short Term Average Energy to Long Term Average Energy (STA/LTA)
Sweet Spot
Sweet Spot
Many codas for large events

## Slide 14: Coda Model II: Can recognize a coda arrival because its attributes are highly correlated with direct arrival’s attributes
Coda arrival azimuth relative to direct arrival’s azimuth

## Slide 15: Example of results with coda added to the model
Before: NET-VISA produced 5 events.
After: Only one event is produced from same sequence of arrivals.
NET-VISA events
LEB event
Notes: Python debug.py 492 leb 5297214

## Slide 16: NET-VISA performance before and after coda model
Before
After
SEL3
% of events that were found that were true.
% of true events that were found
Threshold for declaring an event has been found
Coda model significantly reduces the number of false events produced by NET-VISA while continuing to find 90% of true events. Both implementations outperform SEL3.

## Slide 17: Percentage of Missed Events by Event Magnitude
Chart: 
| unknown | 2 -- 3 | 3 -- 4 | 4 -- | all
SEL3 | 35.1 | 50 | 33.5 | 13.4 | 30.3
NET-VISA | 9.5 | 11.1 | 13.4 | 7.9 | 11.8
Percentage Missed
Body-wave magnitude
SEL3 misses 30% of LEB events. NET-VISA with coda model misses 12% overall and 5x improvement in detection of small events (that took place close enough to network stations to be detected).
Notes: (Revision 212)

## Slide 18: Recall on Continental US
Chart: 
| unknown | 1-2 | 2-2.5 | 2.5-3 | 3-4.5
LEB Recall | 0.231 | 0 | 0 | 0 | 0.077
NET-VISA Recall | 0.231 | 0 | 0.042 | 0.171 | 0.538
Local Magnitude
LEB is missing more than 90% events in the continental USA listed in NEIC (IRIS). NET-VISA finds half of them.

## Slide 19: Conclusions
Adding coda model to NET-VISA significantly improves performance.
  Factor of 3 improvement over SEL3
  Order of magnitude lower detection threshold vs. LEB
  No need to prune spurious events